## Slide 1: Marais des Cygnes RAC meeting
May 2, 2023

## Slide 3: KWA meetings
January-
  Legislative visits
April-
  Upper Arkansas RAC message
  KCC well plugging

## Slide 4: Legislative Update
House Bill 2302
  Adjustments to the State Water Plan Fund
    Additional $35 million from SGF to SWPF
    Transfers $5 million from SWPF to new Water Technical Assistance Fund
    Transfers $12 million from SWPF to new Water Projects Grant Fund
    Guidelines to KWA when making SWPF budget recommendations

## Slide 5: Legislative Update cont.
House Bill 2279
  Annual reports to legislature from GMDs
    Mostly financial documents…. Income, expenses, audits, assets
    Activity descriptions and explanation of how GMD boards are furthering conservation of the groundwater
  Requires each GMD to identify priority areas of concern
    Report to the Chief Engineer
    Action plan for priority areas of concern by July 1, 2026

## Slide 6
TMDLs in the Marais des Cygnes Basin
Dane Boring | May 2, 2023

## Slide 7
1. Define water quality through Water Quality Standards (WQS)
2. Assess available data against the WQS
3. Write TMDL to restore waters from impaired to attaining WQS
Three pollutants and water bodies:
Bacteria in the Marais des Cygnes (near Ottawa)
Eutrophication in Hillsdale Reservoir
Another time: Atrazine in Edgerton City Lake
What is a TMDL?
TMDLs in the Marais des Cygnes

## Slide 8
Bacteria in the Marais des Cygnes near Ottawa
Water Quality Standards (WQS) have adopted bacteria criteria to protect recreational uses (fishable and swimmable).
Marais des Cygnes has those uses protected for primary contact (deep enough to swim in).
Originally listed as impaired for fecal coliform bacteria 20+ years ago. TMDL was approved in 2001
Since then, WQS have changed from fecal coliform to E. coli and KSA 82a-2001.
TMDLs in the Marais des Cygnes

## Slide 9
Bacteria in the Marais des Cygnes near Ottawa (cont’d)
TMDL states Ottawa’s discharge needs UV disinfection to improve bacteria loadings in the stream.
From 2020 to present, Ottawa has averaged 50 cfus/100 mL for E. coli; criteria is 262 in rec season and 2,358 in non-rec season (in other words, not likely to be cause of impairment).
How about the ambient station?
TMDLs in the Marais des Cygnes

## Slide 10
Bacteria in the Marais des Cygnes near Ottawa (cont’d)
SC270 designated in the TMDL
  Quarterly monitoring for E. coli since 2003
  Average value is 879 cfus/100 mL (median is 91.5 and 75th percentile is 283)
  Violations suggest still impaired
KSA 82a-2001 constrains making any impairment decisions
Also of note is WRAPS 9-element Plan for Middle Marais des Cygnes
TMDLs in the Marais des Cygnes

## Slide 11
Hillsdale has been listed for impairment of narrative criteria (“free from”) and a TMDL was written to address Eutrophication (excess nutrients).
The TMDL states all uses impacted to an extent by the eutrophication.
Eutrophication in Hillsdale
TMDLs in the Marais des Cygnes

## Slide 12
First TMDL written in 2001, revision done in 2013
  Chl-a endpoint of 10 µg/L was chosen for the TMDL; median since 2001 has been 19 µg/L
Sets lbs/day limits from wastewater plants
  Normally a concentration like E. coli, but nutrients are about total pounds going into the reservoir
Population of Gardner 2000: 9,800
Population of Gardner 2020: 23,400
Eutrophication in Hillsdale
TMDLs in the Marais des Cygnes

## Slide 13
Also of note: WRAPS 9-element for Hillsdale
Eutrophication in Hillsdale (cont’d)
TMDLs in the Marais des Cygnes

## Slide 14
Thank you/Questions
TMDLs in the Marais des Cygnes